Building Oscillating Circuits
(multivibrators)
Using Transistors

---
Introduction
Blah blah...

---
What's a multivibrator?
- Circuit that has multiple states,
  and changes between them
- Our circuits have 2 states
- Stable – won't change away from a state
  without external action
  - Bistable – Stable in both states (Bi: 2)
  - Monostable – Stable in just one state (Mono: 1)
  - Astable – Stable in neither state (A: Not)

---
LED Circuit

---
(Bipolar) Transistors
- Explain transistors
  3 pins, CBE (Collector Base Emitter), electronic switch, B controls connection between C, E.
- Voltage controlled
- Transistor has resistance, so applying V causes I, so often considered current controlled
- Amplifies current (RCE varies based on VBE)
- NPN, PNP

---
Transistor Circuit

---
Bistable Circuit

---
Bistable Animation
http://www.falstad.com/circuit/e-multivib-bi.html

---
Monostable Circuit

---
Monostable Animation
http://www.falstad.com/circuit/e-multivib-mono.html

---
Astable Circuit

---
Astable Animation
http://www.falstad.com/circuit/e-multivib-a.html

---
Let's Build Circuits!

---
Breadboard Layout
Describe how breadboard is hooked up

---
Placing components
- Polarity
- Don't bend pins
- Don't burn out LEDs
  by connecting to power with no resistor
- Don't connect power until complete

---
Transistor Packages
E-line package
Kit contains:
ZVP2110A (we won't use this)
TO-92 package
Kit contains:
BC547 (use this; has pink dot on back)
BS170 (we won't use this)

---
Bistable – Step 1
FIXME: Text

---
Bistable – Step 2

---
Bistable – Step 3

---
Bistable – Step 4

---
Bistable – Final

---
Test istable
- Apply power
  Note heat-shrink colors
- Use flying wire to connect ground to (right hand lead of) each LED. Observe bistable nature

---
Monostable – Step 1

---
Monostable – Step 2

---
Monostable – Final

---
Test Monostable
- Apply power
  Note heat-shrink colors
- Use flying wire to connect ground to (right hand lead of) each LED. Observe bistable nature

---
Astable – Step 1

---
Astable – Step 2

---
Astable – Final

---
Test Astable
- Apply power
  Note heat-shrink colors
- Observe astable nature

---
Questions