Let's build circuits!

---
Welcome
- Today we will build some electronic circuits
- Four different circuits
  - Choose which you want based on experience
  - Light an LED
  - Control an LED using a switch
  - Build a NOT logic gate (inverter)
  - Flash an LED

---
Breadboards
- Used for quick circuit prototyping
- Has holes to plug components' wires into
- Internal wires connect the holes in a predefined pattern
Main circuit building area
Gutter for ICs
(not used today)
Power rails along edges
Main body is columns
of 5 connected holes
Two sides of gutter not connected

---
Placing components
- Polarity
  - Some components don't work backwards;
    follow instructions in handouts
- Don't bend pins
  - Gentle aiming OK, no need for permanent kinks
- Carefully connect circuits as shown
  - Or you may burn out a component
- Don't connect power until circuit is complete

---
Transistor Packages
E-line package
Kit contains:
ZVP2110A (used in NOT gate)
TO-92 package
Kit contains:
BS170 (used in NOT gate)
BC547 (use in LED flasher; has pink dot)

---
Start Building
- You will need:
- Circuit handout(s)
- Breadboard
- Bag of components
- Power supply (USB)
- Power cable (modified USB)