NOT gate – Step 1
Both components far back against gutter
Components are adjacent, not sharing columns
LED:
Flat side, short lead
on right
Switch:
Wires stick out of top and bottom of switch, not left and right

---
NOT gate – Step 2
LED:
Flat side, short lead
on right
Far back against gutter
One column gap between each LED and the transistors
P-channel transistor (flat back, no pink dot)
Larger flat side facing you
Overlaps N-channel transistor in one column only
N-channel transistor (round back, no pink dot)
Flat side facing you
Overlaps P-channel transistor in one column only

---
NOT gate – Step 3
Add four Wires
Pay careful attention to exactly match the picture

---
NOT gate – Step 4
Add three Wires
Pay careful attention to exactly match the picture

---
NOT gate – Step 5
Resistor 10KΩ:
Brown black black red
In the same column as the switch's right wires
Resistor 150Ω:
Brown green
black black
In the same column as each LED's right wire

---
NOT gate – Step 6
Plug in power once circuit is complete
Pay attention to the colors of the two wires
Observe the two
LEDs' behavior
when the switch
is pressed and
released

---
NOT gate – Analysis
- The left LED is the circuit's input
- The right LED is the circuit's output
- When the switch is not pressed, what state are the input and output? (Each is “on” or “off”)
- When the switch is pressed, what state are the input and output now?
- How does the output relate to the input? (unrelated, always on, always off, same, or opposite)