Bus Protocols Explained
Parallel, '232, I2C SPI
Stephen Warren

---
Contents
- Brief discussion of binary
- Parallel bus
- RS-232/EIA-232 (serial)
- I2C
- SPI

---
Binary

---
Representing Numbers: Binary
- Signals in (most) digital circuits have two states:
  - On/off, high/low, 1/0
- This maps perfectly to binary math:
  - Binary allows only two values for any digit
  - 1 and 0
- What is binary?
  - Simply another way to represent numbers
  - Math works exactly the same

---
Binary vs. Decimal
- Decimal uses 10 values for digits; 0..9
  - Numbers are represented as a sum of powers of 10
  - 90510: (9 ∙ 102) + (0 ∙ 101) + (5 ∙ 100)
- Binary uses 2 values for digits, 0..1
  - Numbers are represented as a sum of powers of 2
  - 1012: (1 ∙ 22) + (0 ∙ 21) + (1 ∙ 20)
- Circuits use a fixed number of digits per number
  - Each digit is a single wire/signal in the circuit
  - Using 8 bits (1 byte) is common; matches files, ASCII, ...

---
Binary Examples
- 000000002 = 010
- 000000012 = 110
- 000000102 = 210
- 101001102 = 16610
- 111111112 = 25510

---
Simple Parallel Port/Bus

---
Simple Parallel Port - Signals
- Used by (older) printers
- More complex variants are possible
  - Address, read-vs-write, wait/busy, …
  - Other uses: Memory bus, PCI, ...
d[7:0]
Master
Slave
strobe
(ground connection is implicit in all diagrams)

---
Simple Parallel Port - Waves
- Data sent via d[8:0] signals
  - 8 bits are sent at once “in parallel”
- Strobe signal pulses once
  for each byte to transfer

---
RS-/EIA-232

---
RS-232/EIA-232 - Signals
- Data is “serialized” onto a single signal
- Asynchronous; no clock or strobe
  - Start and Stop bits used for sync; see waves
- Bi-directional; independent communication
  in each direction
txd
rxd
Device A
Device B
rxd
txd

---
RS-/EIA-232 – (TTL) Waves
- Idle state is “1”
- 1 start bit
- 5, 6, 7, or 8 data bits sent serially LSB first
- Optional odd/even/mark/space parity bit
- 1, 1.5, or 2 stop bits

---
RS/EIA-232 – Baud Rate
- Each bit takes a fixed time to transmit
- The transmitter and receiver must agree
  on the time taken for each bit
- The baud rate is the measurement of this time
  - Counted in terms of bits per second, e.g. 115200
  - Defines how many bits fit into each second,
    and hence the time taken by each bit

---
RS/EIA-232 – Voltage Levels
- TTL and true RS-232 use different voltages,
  but the same protocol
- TTL: a 0 is 0V, a 1 is e.g. 1.8V, 3.3V, 5V
- RS-232: Depending on what you read:
  - 0 is at least +3V, perhaps up to +25V
  - 1 is at least -3V, perhaps down to -25V

---
RS/EIA-232 – Receiver Sync
- No clock; receiver must sync to incoming signal
- RX typically samples using clock running at 16x baud rate to align to beginning of start bit
- Start bit re-sampled 8 clocks later
- Each bit sampled at 16 clocks later
- Start, parity, stop bits validated before accepting character

---
I2C
a/k/a TWI
http://www.i2c-bus.org/

---
I2C - Signals
- Multi-master, multi-device
- One clock line (scl), driven by master
  - Possibly extended by slave
- One data line (scl), bi-directional
Pull-ups
scl
sda
Master
Slave
Master
Slave

---
I2C - Signaling
- Open-collector: Each device can either:
  - Actively pull the line to logic 0
  - Not drive the line; pull-up resistors pull the line to logic 1
- No electrical conflicts with multiple drivers!

---
I2C - Waves
- Start bit: Data falls while clock high
- 7 device address bits, 1 read/write bit, 1 ack bit
- 8 data bits, 1 ack bit
  - Meaning of data bits is up to the device
  - Can be repeated many times
- Stop bit: Data rises while clock high

---
I2C – Protocol
- I2C defines the pieces (start, stop, read, write)
- Devices define their own protocol details
- Common simple devices:
  - Write: Start, write device address, write data, stop
  - Read: Start, write device address, read data, stop
- Common register-based devices:
  - Write: Start, write device address, write register address, write register data, stop
  - Read: Start, write device address, write register address, repeated start, read register data, stop

---
I2C – Clock Stretching
http://www.i2c-bus.org/i2c-primer/clock-generation-stretching-arbitration/
- Master pulses the clock to drive the transaction
- When the clock is low, the device can “stretch” the clock by pulling it low too
- The master will notice this,
  and wait until the device releases the clock
- This allows slow slaves to operate
  at the clock speed they wish
- Also could be used to delay a response until e.g. an ADC conversion is complete

---
I2C – Multi-Master
http://www.i2c-bus.org/i2c-primer/clock-generation-stretching-arbitration/
- Any master can start a transaction
  when the bus is idle
- If no other master starts at the same time,
  the transaction simply operates as expected
- If multiple masters start at once,
  some master sees the bus in a different state than it is transmitting
- That master simply aborts its transaction and lets the other master keep going
  - The transaction will be retried once the bus is idle

---
I2C – Repeated Start
http://www.i2c-bus.org/repeated-start-condition/
- Bus is idle between stop and start
- Master can lose bus ownership (arbitration) when idle
- Can be a problem for register reads
  - This takes two separate I2C transactions
  - Register address could be corrupted by another master
- Generate a repeated start to solve this
  - (Generate a start without a stop first; bus never idle)

---
I2C – 10-bit Addressing
http://www.i2c-bus.org/addressing/10-bit-addressing/
- 7 bits of address isn't that much
- Can have address collisions between devices
  - Devices often can be configured to 1 of n addresses
  - Doesn't solve all problems
- Some devices can use 10 bits for the address
  to help avoid collisions (split over 2 bytes)
- Some of the 7-bit patterns indicate
  an extra address byte follows
  - No 7-bit device will respond to those patterns

---
I2C – Clock Rate
- I2C originally used 100KHz clock rate (max)
  - Clock stretching can slow this
  - But devices must be able to handle 100KHz clock,
    even if they stretch the clock when responding
- Protocol revisions allow for devices
  that can handle a 400KHz or 3.4MHz clock
  - This allows faster data transfer
  - Thus bus can ran only as fast as the clock rate supported by the slowest attached device

---
SPI
a/k/a SSP

---
SPI - Signals
- Single-master, multi-slave (chip-/slave-selects)
- Master drives clock
- Read and write use separate wires
  - Master In Slave Out / Master Out Slave In
clk
mosi
miso
Slave
Slave
Master
cs/ss

---
SPI - Waves
- Rising clock: Both master and slave send data
- Falling clock: Both receive a data bit too
- Data typically framed into bytes
  - By counting clocks/bits since start of transaction
- 100% of the meaning of data is defined by the slave device, not by SPI itself

---
SPI with Chip Select - Waves
- Addition of chip-/slave-select signals allows
  multi-slave operation
- Each slave receives MOSI and drives MISO only when its own chip select is active

---
SPI - Modes
- Clock polarity can differ:
  - Referred to as CPOL
  - 0: Clock is 0 at idle, rises and falls for each bit
  - 1: Clock is 1 at idle, falls and rises for each bit
- Clock phase can differ:
  - Referred to as CPHA
  - 0: First edge: send data, second edge: receive data
  - 1: First edge: receive data, second edge: send data
- Together, these define the “mode”

---
SPI - Modes
https://commons.wikimedia.org/wiki/File:SPI_timing_diagram2.svg

---
SPI - Modes
Mode	CPOL	CPHA
0	0	0
1	0	1
2	1	0
3	1	1
Not all vendors agree on the mapping of
mode to CPOL/CPHA values:-(

---
SPI – Clock Rates
- Clock is driven by master; master sets rate
- No clock stretching
- Each slave can only withstand
  a certain maximum clock rate
- The chosen clock must satisfy each slave's requirements re: maximum rate

---
Final Thoughts

---
Voltage
- Each device operates at some voltage
- For I2C, SPI, the voltage is set by the device,
  not the protocol definition
- 5V, 3.3V, even 1.8V are common
- Make sure your devices and controller
  are all compatible!
- Level shifters can let you mix/match devices

---
Bit-Banging
- Dedicated controllers make protocols easy
- Some micro-controllers/CPUs/SoCs/... don't have enough controllers
- You might need to “bit-bang” the protocol
- That is: write software to read/write
  GPIO pins to emulate the protocol
- Typically data rates are lower when bit-banging,
  due to software overhead

---
Other Protocols
- WS2812 RGB LEDs
- OneWire, CAN, infra-red (remote control), ...
- Custom protocols
- Common themes across all protocols
- Interrupts (out-of-band attention requests)

---
Questions