Digital Logic
Build Your Own Logic Gate From Scratch

---
Overview
- Digital Logic vs. Analog
- Digital Data Representation
- Logic Operations, Truth Tables
- Transistors
- NOT gates, NAND gates, …
- Build a Logic Gate

---
Digital Logic vs Analog
- All circuits have two (perhaps more) power inputs;
  0v and e.g. 5v.
- Signals in analog circuits vary arbitrarily between them
- In digital circuits:
  - Voltage represents data
  - Only the two values 0v and e.g. 5v are used;
    values in between aren't used
  - Boolean logic; true/false
  - Binary math
  - 0/low/false (0v), 1/high/true (5v)

---
Logic Operations, Truth Tables
- Logic operations (gates) take a set of inputs, transform them, and produce a set of outputs
- Truth tables define output value(s)
  for each combination of input(s)
- Also: NOR/AND/OR/XOR/XNOR/...
NAND
NOT
A	X
0	1
1	0
A	B	X
0	0	1
0	1	1
1	0	1
1	1	0

---
Transistors
- Many types; Bipolar, BJT, UJT, FET, ...
- CMOS FETs (MOSFETs) used for most modern ICs
- Think of MOSFETS as a simple switch;
  they conduct between 2 terminals (source/drain)
  or not, based on a control voltage (at the gate)
- Two types of MOSFET:
  - N-channel conducts if gate input is high
  - P-channel conducts if gate input is low

---
NOT schematic
NOT
A	X
0	1
1	0

---
NAND schematic
NAND
A	B	X
0	0	1
0	1	1
1	0	1
1	1	0

---
Questions

---
Build A Logic Gate!
You will need:
- Bag of components
- Breadboard
- USB power supply
- Modified USB cable

---
NOT gate - Step 1
LED
Flat side, short leg
to ground
Switch
Fit into 3x3 block
terminals at top/bottom
Wire
Wire

---
NOT gate - Step 2
10KΩ resistor
150Ω resistor

---
Transistor Packages
E-line package
Used by our P-channel device
(straight legs)
TO-92 package
Used by our N-channel device
(bent legs)

---
NOT gate - Step 3
P-channel FET
(E-line, straight legs)
Flat side facing you

---
NOT gate - Step 4
N-channel FET
(TO-92 bent legs)
Flat side facing you

---
NOT gate - Step 5
Wire
Wire
Wire
Wire

---
NOT gate - Step 6
LED
Flat side, short leg
to ground
Wire
150Ω resistor

---
NOT gate - Power!
USB power cable
note heat-shrink colors!

---
NOT gate – Test
- Press and release the button to test the NOT gate
- Verify that the input and output match the truth table
NOT
A	X
0	1
1	0

---
Questions

---
NAND gate – Step 1
LED
Flat side, short leg
to ground
Switch
Fit into 3x3 block
terminals at top/bottom
Wire
150Ω resistor
10KΩ resistor
Wire

---
NAND gate – Step 2
LED
Flat side, short leg
to ground
Switch
Fit into 3x3 block
terminals at top/bottom
Wire
150Ω resistor
10KΩ resistor
Wire

---
Transistor Packages
E-line package
Used by our P-channel device
(straight legs)
TO-92 package
Used by our N-channel device
(bent legs)

---
NAND gate – Step 3
P-channel FET
(E-line, straight legs)
Flat side facing you
N-channel FET
(TO-92 bent legs)
Flat side facing you

---
NAND gate – Step 4
N-channel FET
(TO-92 bent legs)
Flat side facing you
Wire

---
NAND gate – Step 5
LED
Flat side, short leg
to ground
150Ω resistor
Wire

---
NAND gate – Step 6
Wire

---
NAND gate – Power!
USB power cable
note heat-shrink colors!

---
NAND gate – Test
- Press and release the buttons to test the NAND gate
- Verify that the inputs and output match the truth table
NAND
A	B	X
0	0	1
0	1	1
1	0	1
1	1	0

---
Questions