Introduction To Electronics
A practical introduction to
common electronic components and circuits

---
Overview
- Concepts – Circuit, Current, Voltage
- Basic Components
- Build simple circuits
- Experiment with components

---
Level Of Detail
- Brief description of theory
  - Nothing too heavy
  - Plenty of opportunity for follow-on presentations
    or hands-on coaching
- Practical familiarity with components
  - Pick them up and look at them a bit later
- Practical experimentation
  - Hopefully you'll get an intuitive feel
    for what the components do

---
What Is A Circuit?
- A closed loop through which electrical current can flow
  (What's current? Next page...)
- The loop will contain various components
  (We'll describe some examples later...)
- Can be a complex network of loops,
  not just one simple loop

---
Current - 1
- A movement of charge carriers around a circuit
  - Those charge carriers are typically electrons
  - Similar to the flow of water in a pipe
- Measured in Amperes/Amps (A)
  - LEDs or micro-controllers use tens of mA
  - Consumer electronics use (order of) ~1-2A
  - Home appliances use (order of) 10-50A
  - Just a few mA can kill you!
    - Depending on voltage and other factors
    - Don't worry – low voltages are safe

---
Voltage
- “Electric potential energy per unit charge” (wikipedia)
  - Sounds complicated!
  - Potential: cf. gravitational potential energy
    due to height differences in a hydro-electric dam
- Think of it as the force pushing current
  - Similar to pressure in a water pipe,
- Measured in Volts (V). Typical values:
  - 5V for electronics (safe to tinker with)
  - 12V for car batteries
  - 100-250V for household mains (don't play with this)
  - Perhaps 2000kV for grid transmission lines (stay well away)

---
Current - 2
- Current moves charge carriers from areas at one voltage to areas of another voltage
- This is a change in the (electric) potential energy of the charge carriers
- The gained or lost energy can be converted to/from other forms, e.g. light, heat, motion
  - This is how electronics interfaces with the world

---
+
Voltage Sources
5V
GND
Mains electricity
Batteries
Wall Wart / Power Supply / Charger

---
Wires
- Contain lots of charge carriers (electrons)
- Carry current
- Connect components
- Also, traces on PCB
Breadboard wires
have connectors on the end
Many different kinds of wire;
Single/multi-core, shielded/not, ...

---
Breadboards
- Used for quick circuit prototyping
- Holes to plug components' wires into
- Internal wires connect some of the holes
Columns are named
Rows are numbered
Gutter for ICs
Power rails along edges
Main body is rows
of 5 connected holes

---
Resistors - 1
- Restrict the flow of current through a circuit
- Non-polarized: 2 identical terminals (wires)
- Value measured in Ohms (Ω)
  - Typical values zero to millions of Ohms
- Ohm's law:
  - V = IR
  - A voltage of 1V across a resistance of 1Ω causes 1A of current to flow through it
  - Conversely, if a current of 1A flows through a resistor of 1Ω, there is a 1V voltage drop across the resistor

---
Resistors - 2
Common low-power resistor
Value represented by color bands
High power resistor
Value might be written as text, possibly coded
Multiple resistors in one package

---
Resistors - 3

---
LEDs
- Emit light when current flows through them
- Polarized; two terminals are different
  - Anode:	Connect to more positive voltage
  - Cathode:	Connect to more negative voltage
Flat edge, short leg:
Cathode
Bi-color LED;
2 LEDS in 1 package
Anode

---
A Simple Circuit
Schematic
Resistor limits current
to protect LED
Power source (5V)
Power supply implicitly
connected to both 5V/GND
LED emits light
when current flows
Power source (0V/GND)

---
A Simple Circuit
Breadboard
150Ω resistor
Brown, green, black, black
LED: cathode on right
(flat side, short leg)
Count the holes, and match the picture!
It will be easier to make later circuits
USB power supply
Match the heat-shrink colors

---
Different Resistor Values
Breadboard
Does the LED light at all?
(look very closely, in darkness, to check)
Change to 10kΩ resistor
Brown, black, black, red

---
Diodes - 1
- Allow current to flow in one direction
  - Cause a slight voltage drop as the current flows
- Block current flowing in the other direction
  - If reverse voltage gets too high,
    break down and current still flows
- Polarized; two terminals are different
  - Anode & Cathode
  - Current can flow from anode to cathode
  - LED is a Light-Emitting Diode

---
Diodes - 2
Stripe at cathode

---
Diodes
Schematic
New component:
Diode

---
Diodes
Breadboard
Which way around must the diode
be fitted for the LED to light?
Add diode
Change back to 150Ω resistor
Brown, green, black, black
Move wire

---
Switches
Connect (or not) their terminals based on physical position of part of the switch

---
Resistors In Series
Schematic
New component:
Switch
Extra resistor
in series with R1
S1 optionally
bypasses R2

---
Resistors In Series
Schematic
Current flow with
S1 open:
Current flows through
R1 and R2

---
Resistors In Series
Schematic
Current flow with
S1 closed:
Current flows through
R1 only (not R2)

---
Resistors In Series
Breadboard
Replace diode with 150Ω resistor
Brown, green, black, black
Is the LED brighter or darker
with the button pressed?
New wires
Add switch
Legs are on top/bottom,
not left/right

---
Resistors In Parallel
Schematic
S1 optionally adds
R2 to circuit
Extra resistor
in parallel with R1

---
Resistors In Parallel
Schematic
Current flow with
S1 open:
Current flows through
R1 only (not R2)

---
Resistors In Parallel
Schematic
Current flow with
S1 closed:
Current flow split
between R1 and R2

---
Resistors In Parallel
Breadboard
Is the LED brighter or darker
with the button pressed?
Move resistor
It straddles 4 holes,
not 3 like the other!
Move wire
It aligns with nearer resistor

---
Capacitors - 1
+
+
- Can temporarily store electrical (potential) energy
- Can release (or acquire) energy much more quickly, and at a higher current, than batteries
- Some are polarized, some aren't
- Value measured in Farads (F), but Farads are huge
  - Typical values ~10pF through perhaps 10,000μF
- If connected to a power source, will “charge up”
- If power removed, will discharge, and can power a circuit
- Time take to charge/discharge related to value
  useful in timing circuits

---
Capacitors - 2
Value written as coded text
Value written as text

---
Capacitors
Schematic

---
Capacitors
Schematic
Current flow with
S1 closed:
Capacitor “charges”
through LED1, R1

---
Capacitors
Schematic
Current flow with
S2 closed:
Capacitor “discharges”
through R2, LED2

---
Capacitors
Breadboard
LED: cathode on right
(flat side, short leg)
LED: cathode on right
(flat side, short leg)
3300μF capacitor
Stripe on left side
Wire BEHIND
capacitor
Legs on top/bottom,
not left/right
150Ω resistor
Brown, green, black, black

---
Capacitors
Breadboard
How long does it take
to charge/discharge?
Press and hold
to “discharge” capacitor
Press and hold
to “charge” capacitor

---
Different Capacitor Values
Breadboard
Replace with 1000μF capacitor
Stripe on left side
Is the charge/discharge
slower or faster?

---
Capacitors In Parallel
Schematic
Extra capacitor
in parallel with C1

---
Capacitors In Parallel
Breadboard
Is the charge/discharge
slower or faster?
Add 3300μF capacitor
Straddle the same rows
Stripe on left side

---
Capacitors In Series
Schematic
Extra capacitor
in series with C1

---
Capacitors In Series
Breadboard
Is the charge/discharge
slower or faster?
Remove wire
Move 3300μF capacitor

---
Questions

---
Image Licenses - 1
- http://en.wikipedia.org/wiki/File:Batteries_comparison_4,5_D_C_AA_AAA_AAAA_A23_9V_CR2032_LR44_matchstick-vertical.jpegCC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://en.wikipedia.org/wiki/File:Wall-Wart-AC-Adapter.jpg
  Public domain
- http://en.wikipedia.org/wiki/File:A_plug.jpg
  CC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://en.wikipedia.org/wiki/File:Electrical_outlet_with_label.jpg
  CC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://en.wikipedia.org/wiki/File:A_few_Jumper_Wires.jpg
  CC BY SA 2.0 generic
  http://creativecommons.org/licenses/by-sa/2.0/deed.en
- http://commons.wikimedia.org/wiki/File:Cable_Cross_Section.svg
  CC BY SA 3.0
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://en.wikipedia.org/wiki/File:400_points_breadboard.jpg
  CC BY SA 2.0 generic
  http://creativecommons.org/licenses/by-sa/2.0/deed.en

---
Image Licenses - 2
- http://en.wikipedia.org/wiki/File:Resistor.jpg
  CC BY SA 3.0
  http://en.wikipedia.org/wiki/File:Resistor.jpg
- http://en.wikipedia.org/wiki/File:Danotherm_HS50_power_resistor.jpg
  Public domain
- http://en.wikipedia.org/wiki/File:Sil_resistor.png
  Public domain
- http://bit.ly/my-templates
  https://drive.google.com/previewtemplate?id=1lWeBgAR_CIHPSBInJ29pKoF0bN0YCUG2NX6V9EKPN4o&mode=public
  CC BY SA 3.0
  http://creativecommons.org/licenses/by-sa/3.0/
- http://en.wikipedia.org/wiki/File:Verschiedene_LEDs.jpg
  CC BY SA 2.0 generic
  http://creativecommons.org/licenses/by-sa/2.0/deed.en
- http://en.wikipedia.org/wiki/File:Diodes.jpg
  CC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en

---
Image Licenses - 3
- http://en.wikipedia.org/wiki/File:Ceramic_capacitors.jpg
  CC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://en.wikipedia.org/wiki/File:Electrolytic_capacitor.jpg
  CC BY 3.0
  http://creativecommons.org/licenses/by/3.0/
- http://en.wikipedia.org/wiki/File:Tactile_switches.jpg
  CC BY SA 3.0 unported
  http://creativecommons.org/licenses/by-sa/3.0/deed.en
- http://www.flickr.com/photos/g4ll4is/7125837749/sizes/n/
  CC BY SA 2.0
  http://creativecommons.org/licenses/by-sa/2.0/
- http://www.flickr.com/photos/arionfoto/4186043024/sizes/m/
  CC BY ND 2.0
  http://creativecommons.org/licenses/by-nd/2.0/