Building Oscillating Circuits
(multivibrators)
Using Transistors

---
Introduction
- What is a multivibrator?
- Different types (bistable, monostable, bistable)
- Walk through of the circuits
- Build the circuits

---
What's a multivibrator?
- Circuit that has two states, and changes (vibrates, oscillates) between them
- Bistable – Stable in both states (Bi: 2)
  - Moves between states only when forced externally
- Monostable – Stable in just one state (Mono: 1)
  - Moves from state A to B by external force
  - Moves from state B to A after a time delay
- Astable – Stable in neither state (A: Not)
  - Autonomously oscillates between the states

---
LED Circuit
Resistor limits current
to protect LED
Power source (5V)
Power supply implicitly
connected to both 5V/GND
Power source (0V/GND)
LED emits light
when current flows

---
(Bipolar) Transistors
- A transistor can be a switch,
  or electronically controlled variable resistor
- Transistors generally have 3 pins
- For Bipolar transistors, these are named:
  - Collector
  - Base
  - Emitter
- Base voltage controls whether (how much) the
  Collector and Emitter are connected

---
Transistor – Pictures and Symbols
PNP
(Pointing iN Proudly)
NPN
(Not Pointing iN)

---
Transistors - Operation
- Base-Emitter current determines
  Collector-Emitter current
- Transistors often characterized as amplifying current:
  The more Base current flows,
  the more Collector-Emitter current can flow.
- A Base voltage is required
  to cause a Base current to flow
- NPN: Turns on when Base is high (cf. Emitter)
- PNP: Turns on when Base is low (cf. Emitter)

---
Transistor Circuit
If transistor is ON,
LED connected to GND
so lights up
If transistor is OFF,
LED not connected to GND,
so does not light
If Base is HIGH,
transistor is ON
If Base is LOW,
transistor is OFF

---
Bistable Circuit

---
Bistable Circuit
Circuit from before
Circuit from before

---
Bistable Circuit
Voltage here ...
… controls voltage here ...
… controls whether this
transistor is on or off

---
Bistable Circuit
Voltage here ...
… controls voltage here ...
… controls whether this
transistor is on or off

---
Bistable Circuit
Resistors to limit current
flow into transistors' Bases

---
Bistable Circuit
… this voltage is LOW ...
… this voltage is HIGH ...
… this transistor is OFF ...
IF this transistor is ON ...
… and so this transistor
stays ON

---
Bistable Circuit
… this voltage is HIGH ...
… this voltage is LOW ...
… this transistor is ON ...
IF this transistor is OFF ...
… and so this transistor
stays OFF

---
Bistable Circuit
Force high here
to turn on T1, LED1
Force high here
to turn on T2, LED2

---
Bistable Animation
http://www.falstad.com/circuit/e-multivib-bi.html

---
Monostable Circuit

---
Monostable Circuit
Different

---
Monostable Circuit – Stable State
IF T2 is ON ...
… T1 is OFF ...
… so ignore this!

---
Monostable Circuit – Unstable State
… so voltage is LOW
on BOTH sides of C1
(C1 is not charged)
so T2 stays off ...
IF T2 is OFF ...
… T1 is ON ...

---
Monostable Circuit – Unstable State
… C1 charges,
voltage across C1
increases, so voltage
becomes high here
So T2 turns ON
and T1 turns OFF
(circuit flips state by
itself)

---
Monostable Circuit – Unstable State
Force high here
to turn on T1, LED1
(for a while)

---
Monostable Animation
http://www.falstad.com/circuit/e-multivib-mono.html

---
Astable Circuit

---
Astable Circuit
Different

---
Astable Circuit – Unstable state 1
C2 charges ...
and eventually
T1 turns ON,
T2 turns OFF
IF T2 is ON ...
… T1 is OFF ...

---
Astable Circuit – Unstable state 2
C1 charges ...
and eventually
T2 turns ON,
T1 turns OFF
IF T2 is OFF ...
… T1 is ON ...

---
Astable Animation
http://www.falstad.com/circuit/e-multivib-a.html

---
Let's Build Circuits!

---
Breadboard Layout
Describe how breadboard is hooked up

---
Placing components
- Polarity
  - Some components don't work backwards
- Don't bend pins
  - Slight angling OK, no need for kinks
- Don't burn out LEDs
  - By connecting to power with no resistor
- Don't connect power until circuit is complete

---
Transistor Packages
E-line package
Kit contains:
ZVP2110A (we won't use this)
TO-92 package
Kit contains:
BC547 (use this; has pink dot on back)
BS170 (we won't use this)

---
Bistable – Step 1
6 hole gap
horizontally
At least 3 hole gap
horizontally to edge
BC547 (pink dot)
Flat side towards you
Red line nearest you

---
Bistable – Step 2
LED: cathode on right
(flat side, short leg)

---
Bistable – Step 3
Wire
10kΩ resistor
Brown, black, black, red

---
Bistable – Step 4
Wire
10kΩ resistor
Brown, black, black, red

---
Bistable – Final
Wire
150Ω resistor
Brown, green, black, black

---
Bistable – Test
Apply power
Match heat-shrink colors
Touch wire from POWER … to either LED's right pin
One pin at a time

---
Monostable – Step 1
Delete rear wire, resistor

---
Monostable – Step 2
10kΩ resistor
Brown, black, black, red
10μF capacitor
Negative pin (stripe) on left

---
Monostable – Final
Wire

---
Monostable – Test
Apply power
Match heat-shrink colors
Touch wire from POWER … to left LED's right pin
Wait for LEDs to change automatically

---
Astable – Step 1
Delete rear wire, resistor

---
Astable – Step 2
10kΩ resistor
Brown, black, black, red
10μF capacitor
Negative pin (stripe) on right

---
Astable – Final
Wire

---
Astable – Test
Apply power
Match heat-shrink colors
Observe circuit switching back and forth
between two states automatically

---
Questions